## Slide 1
Jeremy Giffin
Deschutes Basin Watermaster
Oregon Water Resources Department
Carolyn Sufit
Central Region Manager
Oregon Water Resources Department
TSID Water Update

## Slide 2: Talk Outline
Region Overview
Regional OWRD Role
Central Oregon’s Hydrologic History
Water Law/Water Rights Overview
TSID Water rights
Challenges
Drought
Conservation Efforts
2026 Water Outlook

## Slide 3: Central Region
District 11
Deschutes Basin
District 24
Crooked Basin
Notes: Fully allocated surface water
1:1 surface water to groundwater connection
Competing water needs vs water scarcity
Canal infrastructure is some of the oldest and leakiest in the state
Leads the state in conservation efforts
Deschutes Basin Habitat Conservation Plan

## Slide 4: Central Region Overview
~60 active gaging stations
11,727 Square Miles
~3,500 Water rights
~125,000 acres of groundwater rights
~260,000 acres of surface water rights
Notes: ~60 active gaging stations in the region
Inflow, outflows, and district diversions
  Basin conditions
  Forecast basin water budget
Heavy measurement workload
  Many of the gages below dams or diversions need to be measured bi-weekly to verify flows, all year round
  Validation of data needed as flows and conditions change
  Extremely engaged and educated regional water users

## Slide 5: OWRD Regional Role
Distribution and regulation of surface water and groundwater
Regulation and curtailment in times of shortage
Monitor daily river flows and reservoir contents
Basin Storage Report
Dam Safety Inspections
Well Inspections
Notes: Deschutes Basin watermaster (OWRD-state agency) has regulated and distributed the flows of the Deschutes basin for over 100 years.
Regulate Groundwater withdrawals of the Deschutes Basin
Monitor daily river flows and reservoir contents to rapidly respond to agricultural and environmental needs (HCP) and instream water rights
Guide hydrographic-related monitoring to accurately and quantitively for informed decision making through our network of 60 stream gages
Coordinate reservoir releases for irrigation demand with irrigation districts
Provide monthly storage report to irrigation districts to track all water usage
Curtail junior users in times of shortage

## Slide 6: Deschutes History
Central Oregon largely passed by
Carey Act (1894)
Reclamation Act (1902)
Deschutes River fully appropriated (1913)
Reservoir development(1922-1949)
Gentleman’s agreement (1962)
Instream water rights act (1987)
Shift from timber and agriculture to scenic recreation in modern times

## Slide 7: Carey Act (1894)
Oregon accepted the Carey Act in 1901 on condition that private developers front the capital to make the project viable.
Citizens given 160 acres of land as long as you irrigated at least 20 acres.

## Slide 8: Geology and Geography
High Cascades
  150 -200” precip/year
High Desert
  Young lavas, tuffs, sands, gravels (very transmissive)
Large, porous “sponge” creates Deschutes aquifer
Spring fed system
  Attenuated spring flow = drought resiliency
  Minimal surface water flows

## Slide 9: Deschutes River Basin: Surface and groundwater interaction

## Slide 10: Groundwater Recharge
Where does aquifer recharge happen to give us our Deschutes River and robust aquifer?
Gains and Losses surface-groundwater in the upper watershed to Bend.
Groundwater reemerges around Crooked River Ranch, Opal Springs area

## Slide 12: Upper Deschutes Groundwater Study and Mitigation
Upper Deschutes Zone of Impact
USGS/OWRD Ground Water Study 1998
  direct connection between surface water and groundwater, thus Scenic Waterway would be affected by any new ground water rights.
Mitigation required for new ground water rights in the Deschutes Basin study area.
  September 13, 2002 rules adopted for mitigation and mitigation banks (Division 505 and 521).
  HB 3494 passed in 2005 confirming mitigation rules..
Surface water
Groundwater
Fall River
Well

## Slide 13: Groundwater Mitigation
Offset new consumptive use with existing surface water right
2005 appeals ruling overturns rules
HB 3494
Met 50% of the time
Zones of impact
200 CFS mitigation cap

## Slide 14: Groundwater Trends
Chart: Estimated Relative Contribution to Groundwater Declines in Redmond Area (Gannett and Lite, 2013)
| Climate | Pumping | Canal Lining
 | 65 | 25 | 10
*Canal lining as of 2016

## Slide 15
Groundwater Trends

## Slide 16
Groundwater Trends

## Slide 17
Groundwater Trends

## Slide 19: Water Right Development History: Oregon
Pre 1909
  Court based
  Disputes settled through court decrees and adjudications
1909-Present
  State administered permit process
  Requires approval before new water appropriations
  Centralized records
  Formalized prior appropriation

## Slide 20: Key Tenets of Oregon Water Law
Public Resource
First in time, first in right (priority)
Beneficial use without waste
Appurtenance
Water must be used
Notes: One of the key tenets of water law is that all water belongs to the public. With some exceptions, cities, irrigators, businesses, and other water users must obtain a permit or license from the Water Resources Department to use water from any source. This applies regardless of whether the water is groundwater or from lakes or streams.
[time: 24 seconds]

## Slide 21: Key Tenets of Oregon Water Law
Public Resource
First in time, first in right (priority)
Beneficial use without waste
Appurtenance
Water must be used
Notes: We previously discussed the prior appropriation doctrine, or first in time, first in right. This slide shows the earliest priority date that is satisfied after regulation on one stream in each water basin. This is the worst-case scenario in each basin, but in general, surface water in many places in the state has been over-allocated for over 100 years. There has not been enough water in most years to meet surface water rights issued since the mid to late 1800s in the east and southwest parts of the state. In the wet northwest part of the state, there has not been enough water in most years to meet surface water rights issued since the mid-1900s. An early priority date is significantly advantageous in water scarce years.
[time: 45 seconds]

## Slide 22: Key Tenets of Oregon Water Law
Public Resource
First in time, first in right (priority)
Beneficial use without waste
Appurtenance
Water must be used
Irrigation
Domestic
Municipal
Wildlife
Fish Life
Livestock
Recreation
Industrial
Mining
Power
Commercial
Wetland Enhancement
Public Instream Use
Pollution Abatement
Agricultural
Notes: Beneficial use is the foundation and the limit of a water right. Beneficial use means the reasonably efficient use of water without waste for a purpose consistent with the laws, rules and the best interests of the people of the state. While there is no exhaustive list of beneficial uses, some common beneficial uses are shown on this slide, such as irrigation, fish life, and municipal use. A water right for any of these uses would be limited to the amount of water that could be used without waste.
[time: 28 seconds]

## Slide 23: Key Tenets of Oregon Water Law
Public Resource
First in time, first in right (priority)
Beneficial use without waste
Appurtenance
Water must be used
Permit
Personal Property Right
Certificate
Property Right (appurtenant)
Notes: Another key tenet of water law is appurtenance. We refer to a water right being appurtenant to the land. This means that once a permitted water right is developed and we issue a certificate, it is a type of property right and is attached to the land described in the right. If the land is sold, the water right typically goes with the land to the new owner unless the water right is specifically excluded in the deed.
[time: 23 seconds]

## Slide 24: Key Tenets of Oregon Water Law
Water rights must be used within their terms and conditions at least once every five years
  Otherwise, subject to forfeiture and cancellation
  Exceptions may apply
ORS 540.610
Public Resource
First in time, first in right (priority)
Beneficial use without waste
Appurtenance
Water must be used
Notes: A water right must be used consistent with the terms and conditions of the right. Terms include, but are not limited to, the water source, where the water is accessed, where the water is used and for what purpose, how much water can be used, and when it can be used. Water rights also include conditions to protect the public interest. Failure to beneficially use a water right at least once every five years may result in a forfeited water right. This means the water right may be lost unless the water right holder demonstrates that one or more statutory exceptions apply. For example, the water right holder may provide evidence that they were ready, willing, and able to use the water but were unable to make full beneficial use of the water because water was not available from the authorized source. This could occur because of drought or the water right being regulated off. Another exception to forfeiture includes full use of the right not being necessary due to climatic conditions, such as cooler weather or precipitation.
[time: 47 seconds]

## Slide 25: Transferring a Water Right
Change the place of use, character of use, point of diversion, or add a point of diversion
Maintains original priority date
Analysis of evidence of beneficial use or that the right is not subject to forfeiture
Analysis for injury to another user or enlargement of original right
Notes: The use of water under a water right is restricted to the terms and conditions described in the water right certificate. Permit terms include the source of water and priority date, place of use, point of diversion or point of appropriation (a well), and type of use. For example, if a water right holder establishes the right to irrigate a particular 20-acre tract of land, the water cannot be diverted from a different point or source, nor can it be used to irrigate other land. It cannot be used for any other purpose than the type of use indicated in the water right. The water right holder must file a transfer application with the Department to change a point of diversion, point of appropriation, type of use, place of use, or any combination of these. It is not possible to change a water right's source of water or priority date with a transfer application.
In order to approve a transfer, the transfer applicant must provide evidence that the water right was beneficially used in accordance with the terms and conditions of the water right within the 5 years prior to submittal of the transfer application. In other words, they must demonstrate that they actually used the water right recently. In addition, the transfer cannot result in injury to another user nor result in enlargement of the original water right being transferred. ---
• Injury occurs when, as a result of a transfer, another existing water right no longer receives previously available water to which it is legally entitled.
• Enlargement occurs when a transfer would result in such things as increasing the number of acres irrigated or using a greater rate or volume of water.
If the transfer is approved and the applicant successfully makes the changes, a new certificate maintaining the original priority date is issued.
[time: 1 min, 37 seconds]

## Slide 26: The Water Right Permit System
“Proving Up”
Application
Permit
Certificate
Non-Use
Change How Used
Transfer
Cancellation
A water right holder may change their diversion location, place of use or type of use.
“Priority Date”
When a completed application is received, the priority date is assigned.
With some exceptions, if the water right is not used for more than five consecutive years, it may be considered forfeited and could be cancelled.
If approved, a permit is issued. Water use must begin in accordance with the permit, and the user must submit a report on the beneficial use of the water.
Notes: Obtaining a water right is a 3-step process. First, an applicant submits a water right application. The date we receive a complete application establishes the tentative priority date for any permit that may be issued. Permit issuance starts a clock, which is typically 5 years, during which the permit holder must develop their water right consistent with permit conditions. Within this window, the permit holder complies with any conditions that must be satisfied prior to using water. They develop their water use infrastructure and begin beneficial use of water consistent with the terms and conditions of the permit. An example of what this might look like for a surface water right for irrigation is that the applicant would install their pump or headgate, along with a fish screen to prevent fish from entering the water use infrastructure. They would install these components at the point of diversion prior to taking water from a stream. They would develop their pipeline to transport the water from the stream to their field and may install center pivots. They would then begin irrigating a crop consistent with the terms and conditions of the permit. The user has one year from making full beneficial use of water to submit a report to the Department. The Department reviews this claim of beneficial use and, if the user has successfully proved up on their water use, the Department issues a water right certificate. If a water right holder wishes to change their certificated right, they may file for a transfer. A water right may be subject to forfeiture and cancelled if it is not used for five consecutive years.

## Slide 27
Rainwater from an artificial impervious surface
Emergency fire-fighting
Fish screens, fishways, and fish by-pass structures
Forest management
Land management practices (soil conservation, water quality)
Livestock watering must meet certain conditions
Exempt Uses: Surface Water
Notes: A water right permit or license from the Department is required to use water from any source in the State of Oregon, with some exceptions. These exceptions are called exempt uses and are specified in statute. There are exemptions for both surface water and groundwater. A couple examples of exempt uses of surface water are rainwater collected from a roof, and emergency fire-fighting.

## Slide 28
Exempt Uses: Groundwater
Group or single domestic use (household): Not exceeding 15,000 gallons per day.
Stock watering
Irrigation of lawn and/or garden of a half-acre or less: No more than a half-acre in area. Irrigation of larger areas requires a water use authorization and is not exempt.
  Beginning Jan. 1, 2026, commercial gardens not exceeding a half-acre and using no more than 3,000 gallons per day will qualify as exempt.
Industrial or commercial purposes: Not exceeding 5,000 gallons per day, including the 3,000 gallon per-day cap on commercial gardens of one half-acre or less.
Watering school grounds: < 10 acres for schools located within CGWA
Down-hole heat exchange purposes: A closed geothermal loop to provide source heat.

## Slide 29: Regulating Water Use
Pre-Code Water Rights and Adjudication
  No such thing as a grandfathered water right
Application/Permit/ Certification Process
  Conditions, conditions, conditions
Groundwater Rights
  Mitigation requirements
  Well ID tag requirements

## Slide 30: Well ID Program Requirements
Required since 1996 (ORS 537.789-537.793).
Required to be installed when properties sell.
No fee for a well ID tag.
Unique to each well.
Helps in future searches and water rights
Must provide map with start card (2009 SB 788 required map and $300 Fee)
Fee to maintain well log database

## Slide 32: TSID Water Rights
Main certificate 95971 from Whychus Creek.
Supplemental irrigation Watson Reservoir Certificate 95972.
Watson reservoir storage right Permit R-3902.
Supplemental irrigation GW Certificate 97771.
3 Inline Hydro rights Certificates 87798, 92035 & 95164.
McKenzie canyon reregulating reservoir Certificate 31339.
Other surface water Certificates 298, 79496, 87944 & 88554.
TSID Certificate 95971 (living)

## Slide 33: TSID Challenges
Water supply directed related to snowpack and precipitation
No large scale storage facilities
Lots of other senior users share Whychus Creek.
Large diurnal swings in flow
“Runoff” stream subject to large rain event floods
Does not have a large spring flow to buffer low water years
Lots of Ice issues due to the high cold water
LOTS of other users vs Water Scarcity

## Slide 34: Declaring Drought
How droughts are declared in Oregon
  Under ORS 536.700-780, a drought emergency can be declared by the governor by local (county) jurisdictions
    The statue also allows for a statewide declaration, but that is rarely utilized
  A county generally requests a drought declaration from the Governor
    The Governor then refers the request to the Drought Readiness Council (DRC)
    The DRC works with the Water Supply Availability Committee (WSAC) to evaluate the request

## Slide 35: Declaring Drought
How droughts are declared in Oregon
  Water Supply Availability Committee responsibilities
    Evaluate stream flow, snowpack, reservoir levels, precipitation models, temperature models, etc.
  Drought Readiness Council responsibilities
    Evaluate the request based on condition information from the WSAC, partner agencies, socioeconomic conditions ,etc.
  Both WSAC and DRC then make a recommendation to the Governor to approve or deny the request

## Slide 36: Declaring Drought
How droughts are declared in Oregon
  OWRD is the lead agency for drought emergencies
    A drought declaration under ORS 536 authorizes the use of OWRDs Drought Mitigation tools as described in OAR 690-019 (Drought Mitigation)
  Division 19 details the drought tools available and their applicability
    http://www.oregon.gov/owrd/law/docs/law/oar_690_019.pdf

## Slide 37: Existing Drought Tools
Overview of Drought Specific Tools
  Emergency Water Use Permits
  Temporary Transfer
  Temporary Instream Lease
  Temporary Substitution
  Special Option Agreements
  Temporary Exchange of Water
  Human Consumption or Stock Water Use Preference
  Requiring Development and Implementation of Curtailment or Conservation Plans
Full description / definitions available here: http://www.oregon.gov/owrd/docs/HB4113/Draft_Final_Task_Force_Report_11_1_2016_Final.pdf

## Slide 38: Conservation: Leasing and Irrigation Districts
Most of leasing is with irrigation districts
8 Districts in Central Oregon
Divert about 95% of water
Diversions have been decreasing since 1960’s
Sprinklers, measurement, piping, lining, instream transfers and leases & conservation.

## Slide 39: Conservation Efforts Instream Leasing
Chart: CFS Leased Instream Per Year- Central Region (1998-2025)
| 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025
Total | 2.9864 | 4.6274 | 4.7747 | 32.669 | 30.03 | 50.1048 | 79.0032 | 88.9433 | 93.358 | 86.38 | 91.82 | 69.18 | 78.42 | 88.671 | 92.803 | 74.49 | 62.718 | 62.245 | 59 | 59.432 | 58.24 | 59.3 | 57.985 | 54.248 | 58.21 | 64.9 | 79.8 | 73.263
Notes:   Retains priority date
  Beneficial use the second it goes instream
  Versatility in water management
  Held in trust by the state
  1-5 years, cancel anytime
  Reverts automatically to original use
Tumalo, Whychus and zero protected flow below Bend
Now a healthy fishery on T, W, and 140 cfs in Bend
- 1000 of parcels (maybe brief note on workload)

## Slide 40: Instream Water Rights
Whychus Creek below TSID diversion prior to 1998
1987 Instream Water Right Act
Held in Trust by the State
Applied for By State Agencies-Junior
Bought transferred instream-Senior
Over 200 in Deschutes Basin

## Slide 41: Conservation Efforts Allocation of Conserved Water
Chart: Regional Contribution to ACW
| Deschutes/Crooked- 183.511 CFS | All Other Basins- 115.124 CFS | State Total- 272.06 CFS
Regional Contribution to ACW | 183 | 89
Notes: ACW has been wildly successful in this basin
2/3 of ACW efforts have been in the Crooked and Deschutes basins
Up until the HCP, the ACW was one of the primary mechanisms to putting water in-stream
Why didn’t it work? Middle D was beneficiary, to support HCP flows were needed in Upper D
*not all department grants, includes streams outside of mainstem Deschutes/Crooked

## Slide 42: Conservation Efforts Deschutes Basin Alternative Pathway
Voluntary pathway for conserved water projects in response to HCP requirements
Conserved live flow goes to NUID for irrigation
Equivalent Wickiup storage released by NUID in winter for flow augmentation
Legal protections ensure water stays instream

## Slide 43
Questions?
www.oregon.gov/owrd (our website)
https://apps.wrd.state.or.us/apps/sw/hydro_near_real_time/ (NRT)
www.or.nrcs.usda.gov/snow/data/current.html (SNOTEL)
www.usbr.gov/pn/hydromet/destea.html (Deschutes Basin Interactive Gages)
Jeremy.T.Giffin@Oregon.gov
(541) 306-6885
Aubrey Perry (Watermaster 1933-1960) and Jack Frost (NRCS) measuring snowpack in Dutchman Flat area Circa 1940-1945.

## Slide 44: Thank you!
Presenter’s Name
Email address | Phone number

## Slide 45
Overview of the “teacups” as of March 16 2026:
Wickiup 92% Full
Prineville 71% Full
Ochoco 65% Full
Haystack 80% Full

## Slide 46
SNOWPACK in the PNW as of 3/17/26:
24% of Normal

## Slide 47
Water Year PRECIPITATION in the PNW as of 3/17/26:
81% for the Deschutes

## Slide 48
SNOWPACK in the Upper Deschutes
Black Line is this year
Green line is average
21% of Normal

## Slide 49
PRECIPITATION in the Upper Deschutes
Black Line is this year
Green line is average
77% of Normal

## Slide 50
Temperatures

## Slide 51
Three Creek
Meadows SNOTEL
Site 5680’
Three Creek Meadows SNOTEL Site hit ZERO Snow on March 7. When’s the last time that happened?
SWE (inches)
Year
Three Creek Meadows SNOTEL SWE
On March 7 of every year since 1980

## Slide 52
Water in the Upper Deschutes over the last 10 years

## Slide 53
*Using Water Years 1981-2025
*
*
*
The Importance of Natural Flow, Little Deschutes River
Discharge (cfs)
Water Year
~100,000 ac-ft of
Live flow for irrigation season

## Slide 54
“If we get 30” of water in the snowpack at Cascade Summit by April 1st we will be alright.”-Awbrey Perry Deschutes Watermaster 1933-1960.
Snow Water Equivalent
(SWE) inches
April 1
Mar 17

## Slide 55
Annual Volume AC-ft Benham Falls
Water Year
Annual Volume AC-ft Fall River
Benham Falls
Fall River